## Slide 1: ATN Applications: Montgomery County, Maryland Transit Opportunities
Advanced Transit Association Annual Technical Meeting
January 11, 2014
College Park, Maryland
Robert Johnson
R. E. Johnson Consulting Rockville, Maryland www.REJConsult.com

## Slide 2: Basic Assumptions
Proven technology that can be deployed immediately
  25 mph (40 kph) maximum speed
  Small networks
Shared vehicles, especially during peak periods, to increase capacity
All seated -- allows higher acceleration and jerk levels, which means shorter guideway ramps
4-passenger vehicles – a small vehicle allows a narrow, low-cost guideway

## Slide 3: Example of Narrow ATN Guideway

## Slide 4: Montgomery County, Maryland
998,000 population
$94,000 median household income
Immediately Northwest of Washington, DC
21% population growth expected by 2040
39% employment growth expected by 2040
Served by Red Line of Washington Metrorail
Peak hour flows to/from I-270 corridor

## Slide 5: Planned Montgomery County Bus Rapid Transit System
Corridor Cities Transitway, Lines 1-10
102 miles, 79% dedicated lanes
2011 Parsons Brinckerhoff study recommended guided buses in some corridors
Selected peak link volumes:
  Line 7 (Randolph Rd) western section: 900 pphpd
  Line 9 (US 29): 1475 pphpd
Issue: Finding right-of-way for dedicated bus lanes

## Slide 8: Human Genome Sciences Buildings at the Shady Grove Life Sciences Center

## Slide 10: CCT ATN System Benefits
Improve access for many (but not all) Life Sciences Center trips
Avoid two-way bus crossing of major arterial at two locations
Shorter trip times for CCT riders who bypass LSC
Allow uniform CCT headways
LSC internal circulation

## Slide 12: Automated Transit Line to Replace BRT Line 7 Between Branches of the Red Line

## Slide 13: Center Platform Station Geometry Assuming All-Seated Passengers

## Slide 17: Cameron Street in Silver Spring CBD

## Slide 18: Summary of ATN Systems
 | Lane miles* | Stations
Corridor Cities Transitway | 4 | 6
BRT Line 7 (Randolph Rd) | 8 | 5
BRT Line 9 (US 29) | 9 | 3
*Not including on/off ramps, vehicle storage, etc. |  |